## Slide 1: Diffeomorphic registration implementations
Three different methods:
  DARTEL
  ANTS SyN
  Greedy
How they differ in:
  Faster approximations to the LDDMM transformation model
  Image cost functions
  Practical issues

## Slide 2: Fast approximations to LDDMM
As we have seen, LDDMM needs to optimize the entire time-dependent velocity flow at each gradient descent step
This requires a large amount of memory and time
Most registration methods take some shortcuts to make the computations more tractable
Eulerian vs Lagrangian view

## Slide 3: DARTEL
Implemented in SPM
Slides taken from: https://www.fil.ion.ucl.ac.uk/~john/misc/dartel.ppt
Papers:
  DARTEL: Ashburner. A fast diffeomorphic image registration algorithm. NeuroImage, 2007
  Shoot: Ashburner, Friston. Diffeomorphic registration using geodesic shooting and Gauss–Newton optimization. NeuroImage 2011.

## Slide 4: Principles
Diffeomorphic
Anatomical
Registration
Through
Exponentiated
Lie Algebra
Deformations parameterized by a single flow field, which is considered to be constant in time.

## Slide 5: DARTEL
Parameterising the deformation
φ(0)(x) = x
φ(1)(x) = ∫ u(φ(t)(x))dt
u is a flow field to be estimated
t=0
1

## Slide 6: Euler integration
The differential equation is
  dφ(x)/dt = u(φ(t)(x))
By Euler integration
  φ(t+h) = φ(t) + hu(φ(t))
Equivalent to
  φ(t+h) = (x + hu) o φ(t)

## Slide 7: Flow Field

## Slide 8: For (e.g) 8 time steps
Simple integration
φ(1/8) = x + u/8
φ(2/8) = φ(1/8) o φ(1/8)
φ(3/8) = φ(1/8) o φ(2/8)
φ(4/8) = φ(1/8) o φ(3/8)
φ(5/8) = φ(1/8) o φ(4/8)
φ(6/8) = φ(1/8) o φ(5/8)
φ(7/8) = φ(1/8) o φ(6/8)
φ(8/8) = φ(1/8) o φ(7/8)
7 compositions
Scaling and squaring
φ(1/8) = x + u/8
φ(2/8) = φ(1/8) o φ(1/8)
φ(4/8) = φ(2/8) o φ(2/8)
φ(8/8) = φ(4/8) o φ(4/8)
3 compositions
Similar procedure used for the inverse.
  Starts with
  φ(-1/8) = x - u/8

## Slide 9: Scaling and squaring example

## Slide 10: Geodesic shooting
An alternative approach to time-varying (LDDMM) flows
Relies on the conservation of momentum property
  Given the initial conditions, can determine the entire flow

## Slide 11: ANTS Symmetric Normalization (SyN)
Advanced Normalization Tools
  http://stnava.github.io/ANTs/
Papers:
  Avants et al. Symmetric diffeomorphic image registration with cross-correlation: evaluating automated labeling of elderly and neurodegenerative brain. Medical Image Analysis, 2008
  Avants et al. Lagrangian frame diffeomorphic image registration: Morphometric comparison of human and chimpanzee cortex. Medical Image Analysis, 2006

## Slide 12: ANTS Symmetric Normalization (SyN)
Lagrangian optimization instead of Eulerian
  Optimizes the Phi mappings (Lagrangian), instead of the velocity field
    Allowing for larger steps to be taken
  Still computes the velocities (Eulerian), but by pushing the image forward
    Involves inverting the mapping (ie computing Phi inverse) in order to push forward

## Slide 13: ANTS Symmetric Normalization (SyN)

## Slide 14: “Greedy” approach
Algorithm described in Christensen et al (1996); also implemented by Beg
  Modern implementation by Yushkevich
    https://sites.google.com/view/greedyreg
  Eulerian optimization, as in LDDMM
But, instead of optimizing the entire time-dependent flow each step, it uses a “greedy” approach
  Solve timesteps in sequence, one at a time, using the transformation and velocity from the previous step
No geodesic or symmetric properties
  Gains in speed
Not ideal for computational anatomy (i.e. using metrics on the velocity fields/warps), but still very good for simply aligning anatomy

## Slide 15: Image cost functions
DARTEL
  Multinomial image cost based on tissue probabilities
ANTS, Greedy
  Variety of costs available
    Sum of squared differences
    Cross-correlation
    Mutual information

## Slide 16: Summary
DARTEL
  Pros:
    Probabilistic cost function
    Geodesic shooting template generation
  Cons:
    Stationary velocity field transformation could be limiting
    Must use GM+WM probabilities for cost function
    Outputs not interoperable (e.g. SPM-specific formats, MATLAB requirement)
ANTS
  Pros:
    High flexibility (many different transformation models + cost functions implemented)
    Interoperable outputs
    Many wrappers are available (R, python, etc)
  Cons:
    API can be intimidating, many different ways of running it
    Computationally-intensive
Greedy
  Pros:
    Fast & easy to use – makes hyper-parameter selection more tractable
    Good amount of flexibility (most of the useful cost functions from ANTS)
    Robust and fast linear registration too
    Interoperable outputs
  Cons:
    Not suitable if you are doing computational anatomy (ie statistics on velocity/momentum/warp fields
    Newer, not recognized by the community yet

## Slide 17: Some practical considerations
FSL, SPM, and ITK all have different conventions on how spaces and warps are defined
  The ITK conventions are widely adopted as the standard
    ANTS and greedy support this
  Tools exist to convert between conventions (e.g. FSL <-> ITK)
Transforming images should be done with concatenated transforms to avoid interpolation error
  Either by supplying all the warps/matrices at once when warping the image, or generating a concatenated warp file
Transforming images (pull) vs surfaces (push) requires different (inverted) transforms

## Slide 18: Demo
http://github.com/akhanf/methods-lunch-spatial-normalization